## Slide 1: DNS History
APARANET utilized a central file HOST.txt.
  Contains name’s to address mapping.
  Maintained by SRI’s NIC (Stanford-Research-Institute: Network –
  Information -Center)
  Administrators email changes to NIC.
    NIC updates HOSTS.txt periodically.
    Administrators FTP (Download) HOSTS.txt.

## Slide 2: DNS HISTORY Cont….
As the system grew, HOSTS.txt had problems with
  Scalability ( Traffic and load)
  Name collisions
  Consistency.
In 1984, Paul Mockapetris released the first version (RFCs882 and 883,
superseded by 1034 and 1035….)

## Slide 3: DNS Hierarchy
DNS uses a hierarchy to manage its distributed database system. The DNS hierarchy, also called the domain name space, is an inverted tree structure, much like eDirectory.

## Slide 4
Top-Level Name Component of the DNS Hierarchy
Top-Level Name Component | Description | Example DNS Domain Name
.com | An Internet name authority delegates portions of the domain namespace under this level to commercial organizations, such as the Microsoft Corporation. | microsoft.com
.edu | An Internet name authority delegates portions of this domain namespace to educational organizations, such as the Massachusetts Institute of Technology (MIT). | mit.edu
.gov | An Internet name authority delegates portions of this domain namespace to governmental organizations, such as the White House in Washington, D.C. | whitehouse.gov
.org | An Internet name authority delegates portions of this domain namespace to noncommercial organizations, such as the Center for Networked Information Discovery and Retrieval (CNIDR). | cnidr.org
.net | An Internet name authority delegates portions of this domain namespace to networking organizations, such as the National Science Foundation (NSF). | nsf.net

## Slide 5: Root Hints
Root hints are DNS data stored in a DNS server. The root hints provides a list of preliminary resource records that can be used by the DNS service to locate other DNS servers that are authoritative for the root of the DNS domain namespace tree.
Root hints are used to prepare servers authoritative for non-root zones so that they can learn and discover authoritative servers that manage domains located at a higher level or in other subtrees of the DNS domain namespace.
These hints are essential for servers authoritative at lower levels of the namespace when locating and finding servers under these conditions.
By default, the DNS Server service implements root hints using a file, named Cache.dns, stored in the %systemroot%\System32\Dns folder on the server computer.

## Slide 6: Zone Resolution
A zone represents a discrete portion of the domain namespace. Zones provide a way to partition the domain namespace into manageable sections and they provide the following functions:
Multiple zones in a domain namespace are used to distribute administrative tasks to different groups.

## Slide 7: What is a DNS Zone ?
Every domain name, which is a
part of the DNS system, has
several DNS settings, also known
as DNS records ,to keep this DNS
records in order, the DNS zone
was created.
Each DNS zone represents a
boundary of authority subject to
management by certain entities.

## Slide 8: Types of DNS Zones
There are 3 types of DNS Zone.
  Primary DNS Zone
  Secondary DNS Zone
  Stub DNS Zone

## Slide 9: Primary DNS Zone
Primary DNS Zone contain a read/write copy of the zone data.
All the DNS records added manually or automatically, are written in
this Primary zone of the DNS server
The data is stored in a standard text file – .txt.
Something essential is that to be able to make changes to the DNS
zone, the Primary zone must be available.

## Slide 10: Secondary DNS Zone
The Slave zone is a read-only copy of the zone data.
The secondary DNS zone can receive the updated records only from
the primary DNS zone of the DNS server.
Secondary DNS zone can be used as a back up.

## Slide 11: Stub DNS Zone
A stub zone is also read-only like a secondary zone, so
administrators can't manually add, remove, or modify resource records on it.
But the differences end here, as stub zones are quite different from secondary
zones in a couple of significant ways.
First, while secondary zones contain copies of all the resource records in the corresponding zone on the master name server, stub zones contain only three kinds of resource records:
    A copy of the SOA record for the zone.
    Copies of NS records for all name servers authoritative for the zone.
    Copies of A records for all name servers authoritative for the zone.

## Slide 12: DNS RECORDS
It is database record that maps a URL to an IP address
It contains the basic information of all elements of a domain system.
Each record has a type, an expiration time, class.
There are different types of records used in DNS. Most commonly used records are:
1. A/AAAA
2.CNAME
3.PTR

## Slide 13
A/AAAA:
A/AAAA is used to translate domain names into IP address.
A is used to specify the IPV4 address and AAAA is used to specify the IPV6 address
EX:
Example.com A 12.30.56.96
Example.com AAAA 0123:4567:89ab:cdef:0123:4567:89ab:cdef

## Slide 14: 2.CNAME: (Canonical NAME)
It is used for creating alias names for the domains.
CNAME record should not be used for a domain that gets a mail, as the mail server deals it with in an odd manner.
MX records cannot refer to CNAME_ defined hostnames.
Ex:
bar.example.com. CNAME foo.example.com.

## Slide 15: PTR(Pointer Record)
It is used to translate IP address to domain name, by reverse DNS lookup.
As a prerequisite to create a PTR record , we need to create a valid A/ AAAA record that points to desired domain of that IP.

## Slide 16: Iterative resolution
client sends query to 1st server if server is authorized to
domain name it sends answer otherwise send IP address of next
server who can resolve query. Now here client sends query to 2nd
server .Client continues this process of sending query to server until
query is resolved.
In recursive client only send query to 1st server then server will send request to next server until query is resolved.
In iterative client is responsible for sending query to different servers until query is resolved.

## Slide 17: Recursive resolution
A recursive query is a kind of query, in which the DNS server, who received your query will
do all the job of fetching the answer, and giving it back to you. During this process, the DNS
server might also query other DNS server's in the internet on your behalf, for the answer.

## Slide 18
DNS server which keeps all root zone is called TLD name server.

## Slide 19: A root server
Located in Amsterdam, , the Netherlands
198.41.0.4 – IPV4
2001:503:ba3e::2:30 – IPV6

## Slide 20: B root server
Located in Budapest, Hungary
199.9.14.201 – IPV4
2001:500:200::b – IPV6

## Slide 21: C root server
Located in Paris, France
192.33.4.12 – IPV4
2001:500:2::c – IPV6

## Slide 22: D root server
Located in London, United Kingdom
199.7.91.13 – IPV4
2001:500:2d::d – IPV6

## Slide 23: E root server
Located at Boston, US
192.203.230.10 – IPV4
2001:500:a8::e – IPV6

## Slide 24: F root server
Located at Melbourne, Victoria, Australia
192.5.5.241 – IPV4
2001:500:2f::f – IPV6

## Slide 25: G root server
Located at Chicago, Illinois, USA
192.112.36.4 – IPV4
2001:500:12::d0d – IPV6

## Slide 26: H root server
Located at Des Moines, Iowa, USA
198.97.190.53 – IPV4
2001:500:1::53 – IPV6

## Slide 27: I root server
Located at Chennai, Tamilnadu, India
192.36.148.17 – IPV4
2001:7fe::53 – IPV6

## Slide 28: J root server
Located at Singapore
192.58.128.30 – IPV4
2001:503:c27::2:30 – IPV6

## Slide 29: K root server
Located at Moscow, Russia
193.0.14.129 – IPV4
2001:7fd::1 – IPV6

## Slide 30: L root server
Located at Tehran, Iran
199.7.83.42 – IPV4
2001:500:9f::42 – IPV6

## Slide 31: M root server
Located at Chimbote, Peru
202.12.27.33 – IPV4
2001:dc3::35 – IPV6

## Slide 32: Working of DNS
Website Request
Ask resolver
Ask root server
Ask TLD server
Ask authoritative name servers
Cache the IP and return it to the browser